## Slide 1: Project 5: I2C Reading an Analog Temperature Sensor with an ADC
Beau Coburn & Aaron Foster

## Slide 2: Objective
Read an analog temperature sensor and display the value on the LCD
  Main controller to sample an analog temperature sensor’s output and produce a moving average of n-samples (user selectable)
  LCD displays sensor output in Celsius
  LED bar does not change, but speed functionality removed
  Locked state, unlocked, user input via keypad the same.

## Slide 3: Code at a Glance

## Slide 5: Main Controller
  Starts in locked state
  RGB LED indicates system status
  Code “6969” to unlock
  Constantly monitors temp sensor every 0.5s
  Once unlocked, system enters idle mode
    Waits for user input
  User can select size of past average temp measurements
  LCD constantly displays updates to the average temperature sensor
    To 1 decimal place
      Multiple bytes per I2C transmission

## Slide 6: Analog Temperature Sensor
  3.3V Input to CMOS integrated-circuit
  Analog output based on temperature
  MSP430 ADC module reads temperature sensor every 0.5s
    Saves temperature value into circular array to average user selected number of values

## Slide 7: LCD Peripheral
  Contrast of screen can be adjusted
  Set to 4 bit mode
  2 line, 5x8 character
  Screen cleared
  I2C Slave (Receives)
  Drives message or command to LCD
    LED Pattern
    Screen Clear
    Toggle Cursor
  Constantly displays average temperature from master controller

## Slide 8: LED Bar Peripheral
Port initialization
Receives I2C transmission (slave)
Drive received pattern
Transition period can be changed based on transmission
Same data as sent to LCD

## Slide 10: Final Result
  Master-slave communications that is capable of:
    Reading an analog temperature sensor
    Constantly displaying the average temperature value over time
    LED bar patterns
    Displaying the current master state on an LCD screen