## Slide 1: Project 4: I2C Compatible Peripherals (LCD and LED Bar)
Beau Coburn & Aaron Foster

## Slide 2: Objective
- MSP430FR2355 as main controller
- Locked system controlled by 4x4 keypad
- Two MSP430FR2310 as Peripherals controlled by I2C
- Controller sends data over I2C to control actions on peripheral MSPs
- Peripherals control LED Bar and LCD screen
- Patterns on LED Bar
- Name of pattern on LCD

## Slide 3: Code at a Glance

## Slide 5: Main Controller
- Starts in locked state
- RGB LED indicates system status
- Code “6969” to unlock
- Once unlocked, patterns can be selected
- Pattern info transmitted over I2C bus (Master)
  First transmission to led bar slave
  Second transmission to LCD slave

## Slide 6: LCD Peripheral
- Contrast of screen can be adjusted
- Set to 4 bit mode
- 2 line, 5x8 character
- Screen cleared
- I2C Slave (Receives)
- Drives message or command to LCD
  LED Pattern
  Screen Clear
  Toggle Cursor

## Slide 7: LED Bar Peripheral
Port initialization
Receives I2C transmission (slave)
Drive received pattern
Transition period can be changed based on transmission
Same data as sent to LCD

## Slide 9: Issues I2C
SCL stayed low outside the transmission buffer
Caused slaves to not respond to called address
Hardware issue with breakout board
Fixed by keeping logic analyzer connected

## Slide 10: Issues Memory
MSP430FR2310 has 1KB ram
Executable memory
Fixed by changing compiler settings and initialization streamlines

## Slide 11: Result
- Multi MSP system operating over serial communication
- LCD and LED Bar driven from I2C
- Can be implemented within a more complex system